## Slide 1: Software Defined Access
By Khawar Butt [CCIE x 7#12353 & CCDE#20110020]
[R/S, Security, Sp, Voice, Storage Networking, Data Center, Wireless]

## Slide 2: Software defined Access (SDA)
Overview of SDA and controller-based networking
SDA Components & Roles
  DNAC
  Fabric Edge Nodes
  Fabric Border Nodes
  Control Plane NODE(S)
  Underlay Network
  Fusion Router
  ISE

## Slide 3
SDA-Based CAMPUS NETWORK

## Slide 4: SDA – Devices – DNAC Controller
Cisco Digital Network Architecture (DNA) Controller – DNAC is a physical appliance that controls the configuration of SDA based networks.
It is responsible for the Discovery & configuration of the SDA Devices.
You control the configuration & Maintenance of the all the switches in the CAMpus fabric from the DNAC.

## Slide 5: SDA – Devices – Fabric Edge NOdes
These are Access layer switches that connect the End-device to the SDA Fabric.
Fabric Edge Nodes are configured & managed by the DNAC.
Fabric Edge nodes include the Cisco Catalyst 3850, 4500E, 9300 & 9400 Series switches

## Slide 6: SDA – Devices – Fabric border NOdes
The fabric border nodes serve as the gateway between the SD-Access fabric site and the networks external to the fabric.
The fabric border node is responsible for network virtualization interworking and SGT propagation from the fabric to the rest of the network.
Fabric Border nodes include the Cisco Catalyst 3850, 6500, 6800 & 9500 Series switches & Nexus 7700 Switch

## Slide 7: SDA – Devices – Control Plane NOde
The SDA fabric control plane node is LISP Map-Server (MS) and Map-Resolver (MR)
The control plane database tracks all endpoints in the fabric site. It associates the endpoints to fabric nodes (Edge Node or Border)
Fabric Edge nodes include the Cisco Catalyst 3850, 6500, 6800 & 9500 Series switches & Nexus 7700 Switch

## Slide 8: SDA – Devices Underlay Switches
The underlay network is defined by the physical switches and routers that are used to deploy the SD-Access network.
All network elements of the underlay must establish IP connectivity via the use of a routing protocol.
Instead of using arbitrary network topologies and protocols, the underlay implementation for SD-Access uses a well-designed Layer 3 foundation inclusive of the campus edge switches

## Slide 9: SDA – Devices – Fusion Router
fusion router is used to perform VRF route leaking between user VRFs and Shared-Services, which may be in the Global routing table (GRT) or another VRF
Shared Services may consist of DHCP, DNS, NTP, WLC, ISE, DNAC components which must be made available to other virtual networks (VN’s) in the Campus
It could be any L3 Device with VRF& BGP functionality

## Slide 10: SDA – Devices – ISE
ISE is an integral part of SDA for policy implementation, enabling dynamic mapping of users and devices to scalable groups and simplifying end-to-end security policy enforcement
ISE integrates with DNAC by using pxGrid and REST APIs for exchange of client information and automation of fabric-related configurations on ISE.
The SDA solution integrates Cisco TrustSec by supporting group-based policy end-to-end, including SGT information

## Slide 11: Workspace Slide